## Slide 1
Digital Electronics
Principles & Applications
Seventh Edition
Chapter 4
Using Logic Gates
Roger L. Tokheim
©2008 The McGraw-Hill Companies, Inc. All rights reserved.

## Slide 2
INTRODUCTION
Logic Circuit from a Boolean expression
Minterm and maxterm Boolean expressions
Boolean expression from a truth table
Truth table from a Boolean expression
Simplifying Boolean expressions
Karnaugh mapping

## Slide 3
INTRODUCTION (continued)
Variations in Boolean expressions
DeMorgan’s theorem
PLDs (programmable logic devices)

## Slide 4
“Tools of the Trade”
for Solving Logic Problems
Gate symbols
Truth tables
Boolean expressions
Combinational logic circuits:
AND-OR pattern of gates
OR-AND pattern of gates
AND-OR pattern of gates
from
Sum-of-products Boolean expression such as:
AB + CD = Y
OR-AND pattern of gates
from
Product-of-sums Boolean expression such as:
(A+B) (C+D) = Y

## Slide 5: Logic Circuit From Boolean Expression
Example:
Draw the AND-OR logic diagram for the Boolean expression:
Step 1: OR AB with CD
Step 2: Add top AND gate
Step 3: Add bottom AND gate
AB + CD = Y
©2008 The McGraw-Hill Companies, Inc. All rights reserved.

## Slide 6
Draw the OR-AND logic diagram for the Boolean expression:
Step 1:
Step 2:
Step 3:
QUIZ
(A+B) • (C+D) = Y

## Slide 7
Sum-of-products form:
Also called the minterm form
Product-of-sums form:
Also called the maxterm form
Boolean Expressions
A • B + C • D = Y
(A + B) • (C + D) = Y

## Slide 8
QUIZ
1. The Boolean expression AB + BC = Y is in __________ (product-of-sums, sum-of-products) form.
2. The Boolean expression (A+B) (B+C) + Y is in __________ (product-of-sums, sum-of-products) form.
3. The Boolean expression (A+B) (B+C) = Y is in __________ (maxterm, minterm) form.
4. The Boolean expression AB + BC = Y is in __________ (maxterm, minterm) form.
sum-of-products
product-of-sums
maxterm
minterm

## Slide 9
Boolean Expression from Truth Table
Write the Boolean expression that describes the logic in this truth table.
Truth Table
Input Output
ABC Y
0 0 0 0
0 0 1 0
0 1 0 1
0 1 1 0
1 0 0 0
1 0 1 0
1 1 0 0
1 1 1 1
Step 1: Focus only on the truth table lines
with outputs of 1.
Step 2: AND the inputs for these two lines
and logically OR the ANDed groups.
Minterm Boolean expression:
A • B • C
A • B • C = Y
+
A B C
A B C = Y
+

## Slide 10
Truth Table
Input Output
ABC Y
0 0 0 1
0 0 1 0
0 1 0 0
0 1 1 0
1 0 0 0
1 0 1 0
1 1 0 0
1 1 1 1
Write the Boolean expression that describes the logic in this truth table.
Minterm Boolean expression:
A • B • C
A • B • C = Y
+
QUIZ
A B C
A B C = Y
+

## Slide 11
QUIZ
Truth Table
Input Output
ABC Y
0 0 0
0 0 1
0 1 0
0 1 1
1 0 0
1 0 1
1 1 0
1 1 1
0
0
0
1
0
0
0
1
1. Write the sum-of-products Boolean expression for this truth table.
______________________________
A’BC + ABC = Y
2. Write the minterm Boolean expression for this truth table.
______________________________
A’BC + ABC = Y

## Slide 12
Truth Table From Boolean Expressions
Fill in a truth table from a minterm Boolean Expression.
Minterm Boolean expression:
Truth Table
Input Output
ABC Y
0 0 0
0 0 1
0 1 0
0 1 1
1 0 0
1 0 1
1 1 0
1 1 1
1
1
1
0
0
0
0
0
Step 1: Place three 1s
in output column.
Step 2: Place five 0s in blanks in output column of truth table.
A•B•C
A•B•C
A•B•C
= Y
+
+

## Slide 13
QUIZ
Truth Table
Input Output
ABC Y
0 0 0
0 0 1
0 1 0
0 1 1
1 0 0
1 0 1
1 1 0
1 1 1
1. Fill in the output column of the truth table for the Boolean expression A’B’C’ + ABC’ = Y.
1
0
0
0
0
0
1
0

## Slide 14
This line is not to be considered in the loop.
This line is not to be considered in the loop.
This line is not to be considered in the loop.
This line is not to be considered in the loop.
Unsimplified Boolean Expression
Simplifying Boolean Expressions
Truth Table
Input Output
ABC Y
0 0 0
0 0 1
0 1 0
0 1 1
1 0 0
1 0 1
1 1 0
1 1 1
0
0
0
0
1
1
1
1
RULE:
Eliminate term within loop that contains a term and its complement.
A•B•C
A•B•C
A•B•C
= Y
+
+
A•B•C
+
Simplified Expression:
A•B
A•C
= Y
+

## Slide 15
_ _
A B
_
C C
_
A B
A B
_
A B
1
1
1
1
C
Simplify Boolean Expression
(Karnaugh map method)
Unsimplified Boolean expression (3 variables):
Step 1: Plot 1s
Step 2: Loop groups
Step 3: Eliminate variables
Step 4: Form simplified
minterm expression
A•B•C
A•B•C
A•B•C
= Y
+
+
A•B•C
+
A C
+
A B
= Y
Simplified Expression:
B
C
B
C

## Slide 16
Simplify Boolean Expression
(Karnaugh map method)
Step 1: Plot 1s
Step 2: Loop groups
Step 3: Eliminate variables
Step 4: Form simplified minterm expression
Unsimplified Boolean expression (4 variables):
_ _ _
C D C D
_ _
A B
_
A B
A B
_
A B
_
C D C D
1
1
1
1
ABCD
ABCD
ABCD
= Y
+
+
ABCD
+
ABC
ACD
Simplified Expression:
+
= Y
QUIZ
B
D
B
D

## Slide 17
Developing a NAND Logic Diagram
Minterm expression: AB + AB = Y
Step 1: Draw AND-OR logic diagram from minterm expression.
Step 2: Substitute NAND gates for each inverter, AND, and OR gate.
NOTE: Both logic diagrams will generate the same truth table.

## Slide 18
Variations in Boolean Expressions
Boolean expression (textbook style):
Boolean expression (keyboard style):
A’B + CD’ = Y
A B + C D = Y
(A + B)’ = Y
A + B = Y
A B = Y
A’ B’ = Y

## Slide 19
QUIZ
1. The Boolean expression A B + C D = Y is written as _______ in keyboard style.
A B’ + C’D = Y
2. The Boolean expression A+B+C = Y is written as _______ in keyboard style.
(A+B+C)’ = Y
3. The Boolean expression A B C = Y is written as _______ in keyboard style.
A’ B’ C’ = Y

## Slide 20
DeMorgan’s Theorems
First theorem:
Second theorem:
A + B = A B
A B = A + B
Both used
to eliminate
long overbars

## Slide 21
DeMorgan’s Theorems
First theorem:
Second theorem:
A + B = A B
A B = A + B

## Slide 22
QUIZ
The statement A B = A + B is DeMorgan’s __________ (first, second) theorem and suggests converting from a NAND to an OR situation.
2. The statement A + B = A B is DeMorgan’s __________ (first, second) theorem and suggests converting from a NOR to an AND situation.
second
first